Shinyei Dust Sensor Air Quality Monitoring
With TI Launchpad MSP430G2

Objective: To know when I need to clean my room. I usually vacuum every two or three weeks, but sometimes am lazy and I need a reminder. The dust sensor will be more motivation to get me to clean, when I see the dust levels increase.

Figure 1: Shinyei PPD42NS Air Quality
Table of Contents:
1. Parts List
2. Work Log

Parts List:
- Shinyei PPD42NS Air Quality Sensor
- MSP-EXP430G2553 V1.5
- 5V Adaptor (required as MSP is 3.3V only)
- SD Card adaptor
- Ethernet Adaptor
- (optional) 16x2 LCD

Work Log

Here are some things I've learned as I've worked on this project.

IDE
I'm using Energia from energia.nu which is an Arduino IDE clone for TI Launchpads. This will allow for rapid development. And ease me into the TI platform.

MSP-EXP430G2 V1.5
There are different version of this. My particular board is the
and as explained here: http://energia.nu/pin-maps/guide_msp430g2launchpad/ and http://energia.nu/pin-maps/guide_msp430g2launchpad/
You need to rotate the UART jumpers to get UART to display correctly. Oddly enough you can choose a different chip in the boards list and serial will print out right... But switch the jumpers and the correct board will work with UART. Otherwise, it does not work out of the box for serial.print. Though the blink example sketch works.

Dust Sensor
The code for the dust sensor is found online easily. The pinout is tricky as the colours of the wire are nonsense, but the pinout seems to be the same for all sensors, and is: PIN 1 (closest to black box) GND, PIN 3, VDD (5+V), PIN 4 output A. there is also an output B for different readings (I think size) of dust. I'm not that particular (no pun intended) about my dust so I will go with the one most people are using.

3.3V only on TI
The TI takes input of USB but only outputs 3.3V. Fail. I'll through a 5V PSU on the board. It won't be connected to USB for its use anyways.