ZMHW Project
Infrared Diode Laser Motion Sensor

Objective: To make a motion sensor that acts as motion detection for Zoneminder cameras. As the cameras often have false alarms, an external sensor is a possible solution. This uses a Laser Diode Infrared Sensor.

Main half of the sensor before putting in enclosure.

Parts List:
Arduino Uno (official recommended)(DIP recommended)
ENC28J60 ethernet module
Passive PoE adaptors for IP Cameras
Series 1A fuse
Sick WS15-D1130 Infrared Laser Diode Motion Sensor
General Purpose Diode (I used 1N4818 diode) (may also use transistor, per data sheet for Sick)
Jumper Wires
Copper Wire (22-26 gauge)
Enclosure
Ethernet Wire
(optional) Low Profile one and two gang wall outlet
(optional) Blank cover plate, for one and two wall gang wall outlet
(optional) Electrical tape (I prefer halfway decent electrical tape)
(optional) piezo speaker
(optional) extras of everything, in case anything fails

Work Log:
This work log will be pictures with some notes thrown in. I'll try to make note of all important parts.

Device was assembled and using the ZMHW Project source code. This is simply an Arduino sketch with UIPEthernet (to use the ENC28J60) (make sure CS is pin 10 on Uno). For more details see source code. Explaining the details is out of the spec of this doc. Simply put, the ENC28J60 is connected, the Sick sensor black wire is connected to Analog input 1, and a speaker is connected. See source code. I will try to put a fritzing diagram in the git repo.
Figure 1: Orange LED on top of sensor when link detected. Series diode on output of sensor to cheat the need for transistor.

Of importance, Figure 1 shows two things, first off a diode connected in series with the output of the Sick sensor, and also the orange LED on the top of the sensor. The
orange led will be green when there is no connection between the diodes and orange when the Laser Diodes (or LEDs) are lined up correctly. When someone moves across the field of their vision, the orange LED will change to green.

Diode on output of Sick sensor
Some laser sensors output a high or low. Some, like the Sick sensor, output a high or low (depending on whether you connect to white or black wire), however they are meant to be connected to a transistor, and thus if you connect it directly to a micro expecting it to go high or low, it will not. I dont want to deal with a transistor as I am lazy, so instead I put a 1N4819 in series with the output of the Sick sensor.
TODO: pictures showing waveforms

Using the black wire, it will be normally low and go high when motion is detected (the white wire is the opposite). If you connect to a micro it will fail to go high (why?). If you put a diode on the end in series, it will turn the normally low to a noisy normally low, and sometimes it will go between 2.5-5 volts in spikes. This allows us to use the ADC to read the Sick sensor, and avoid the use of adding a transistor in. The transistor would allow for a digitalRead to be used, but we have plenty of Analog inputs to use, so let's use one of those.

It's very important to line up these sensors. If they are not lined up precisely, they will not get a sync, and the motion detection will fail. This will become important later, when we install.

Broken ENC28J60
During my testing, I suddenly was unable to get an IP address. I checked the example sketches, then began tearing down my setup, testing another Arduino and ENC module.

It turned out, the ENC28J60 module failed on me. Make sure to buy backups.

Choosing location for the sensors. Keep in mind, that the laser diode path must remain open. This is where the main board and sensor will be.

Feeding nylon string, and a wire up from the bottom of the wall to the ceiling. This is where the single sensor will be.