ZM HWACCEL RPI3 Testing: Amovision Q630M

Objective: To test capabilities of RPI3 with HWACCEL (mmal) enabled, and with a few cameras.

Preface: I’ve already covered the install, and introductory testing in an ascii file. See those for more details in the repo. In this guide we will be testing the Amovision Q630M IP camera. I’ve detailed its good and bad specs at wiki.zoneminder.com.

Test: The Amovision is setup with FFMPEG source, and rtsp path. The path used was found via onvif. One can use either Onvif Device Probe (windows) or the built in ZM Onvif probe.

The configuration is:
Source Path:rtsp://:@10.8.9.223/user=admin_password=SECRET_channel=1_stream=0.sdp
Width: 1280
Height: 720

It was tested and confirmed to work in VLC or Mplayer before trying in ZM.

After adding the camera, using FFMPEG, but no h264 passthrough, we get a resulting load of 3.9 or so, and 23 or 22 FPS. This is a 1280x720 camera.

See image: